Pro Tools 101

Lesson 1 Quiz

Digital Audio and Pro Tools hardware/software

- The bit depth of a digital recording will affect the:

a. Dynamic range

b. Frequency response

c. Phase

d. None of the above

- The sample rate of a digital recording will affect the:

a. Dynamic range

b. Frequency response

c. Phase

d. None of the above

- What would the approximate dynamic range be for a 16-bit recording?

a. 24 dB

b. 48 dB

c. 96 dB

d. 128 dB

- The total number of values represented by a 4 bit word?

a. 2

b. 4

c. 16

d. 32

e. 64

- The frequency of a sound is measured in….

  - cycles per second

  - cycles per sample

  - seconds per cycle

  - seconds per sample

  - none of the above

- Which of the following characteristics of a sound is based upon the harmonic component of its waveform?

  - loudness

  - pitch

  - tone/timbre

  - spaciousness

none of the above

- The set of sine waves that make up a complex waveform are called…

  - fundamentals

  - harmonics

  - periods

  - cycles

  - decibels

- What is the range of human hearing?

  - 10 to 10,000 cps

  - 100 to 100,000 cps

  - 20 to 100,000 cps

  - 100 to 20,000 cps

  - 20 to 20,000 cps

- Which of the following are advantages of recording using a DAW?

  - total recall of all mix and effects parameters

  - more versatile editing capabilities

  - digital signal processing more versatile than with analog processing

  - non-destructive recording

  - all of the above.

- A digital audio sample is …

  - A snapshot of a signal, taken at regular time intervals

  - A snapshot of a signal, taken on an as-needed basis

  - A snapshot of a signal, taken twice every cycle of a sound

  - An average of a signal, taken over it’s full duration

  - An average of a signal, taken within a small time window

- In order to accurately sample a sound within the range of human hearing, the minimum rate is….

  - 20Hz

  - 10KHz

  - 20Khz

  - 40Khz

  - 96KHz

- Which of the following is a reason to consider choosing a high sample rate?

  - Transients contain much higher frequencies than sustained tones.

  - Some signal processing algorithms sound better using higher sample rates.

  - Recordings made with higher sample rates have lower noise.

  - All of the above are reasons to choose a high sample rate.

  - a. and b. only

- The process of assigning a captured value to the closest available amplitude based upon binary word length is called…

  - sampling

  - resolving

  - quantization

  - aliasing

  - conversion

- What are the possible problems caused by quantization?

  - wow and flutter

  - pitch shift and distortion

  - pitch shift and noise

  - distortion and noise

  - noise and print-through

- Which of the following systems are host (or native) based…

  - Pro Tools HD system

  - Pro Tools LE system

  - Pro Tools M-Powered system

  - a. and b.

  - b. and c.

- Being host based means that…

  - They use the Digidesign PCIe cards with digital signal processing (DSP) power for their real-time processing and mixing operations.

  - They use the processing power of the host computer to carry out real-time routing, mixing, and processing of all audio signals.

  - They serve Tea and Crumpets at every session

- Pro Tools LE and M-Powered systems can support sampling rates up to…

  - 192KHz

  - 48KHz

  - 96KHz

  - 44.1KHz

- Pro Tools HD systems can support sampling rates up to…

  - 192KHz

  - 48KHz

  - 96KHz

  - 44.1KHz

- Pro Tools LE and M-Powered systems can support up to…

  - 24 tracks of mono audio (12 stereo)and 256 MIDI tracks

  - 192 tracks of audio and 256 MIDI tracks

  - 32 tracks of mono audio (16 stereo) and 256 MIDI tracks

  - 48 tracks of mono or stereo audio with optional Music Production or DV Toolkit.

  - c. and d.

- Pro Tools LE or M-Powered software will…

  - work with any manufacturers audio interface.

  - only work with Digidesign or M-Audio audio interface hardware.

  - work with HD systems.

- Advantage(s) of an LE or M-Powered system over an HD system are…

  - Low cost

  - Portability

  - Low cost

  - Did I mention low cost.

  - All of the above

- Advantage(s) of an HD system over a LE or M-Powered systems are…

  - More audio track count.

  - Higher sampling rates.

  - More real-time processing.High quality TDM plug-ins

  - Multi-Channel mixing

  - All of the above

- A Pro Tools HD system can...

  - Only use high quality TDM plug-ins

  - Use TDM, RTAS (real time audio suite) plug-ins and AS (AudioSuite) non-real-time plug-ins

  - Can only run on a Mac computer

  - All of the above

- Some Characteristics of Pro Tools systems…

  - Pro Tools LE uses Digidesign hardware

  - Pro Tools M-Powered uses M-Audio hardware

  - Pro Tools HD uses HD software.

  - Can run on both Mac or PC computers

  - All of the above